## Slide 1
Mid-Point Review
ML & NN Analyst Internship · InGen Dynamics
Hongyu Liu · July 2026
Phase A (foundations) and Phase B (neural & sequence models) complete · Phase C (reinforcement learning) next
1 world core
one generator, one canonical
leakage-safe split, one ledger
11 models
6 anomaly detectors + 5 trajectory
regressors, one shared protocol
All gates PASS
100 ms Aido Rover streaming ·
50 ms Aido Humanoid planning
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
1 / 7

## Slide 2
All six models clear the 100 ms gate ≥12× — top F1 0.829 is a capacity effect
Headline · Aido Rover anomaly detection · 7-fold block-rotation mean ± std on the canonical split · single-sample CPU latency
Model | F1 (7-fold) | AUC (7-fold) | ms | ≤100 ms
RandomForest | 0.749 ± 0.048 | 0.960 ± 0.009 | 7.86 | PASS
MLP | 0.794 ± 0.047 | 0.979 ± 0.011 | 0.14 | PASS
1D-CNN | 0.731 ± 0.115 | 0.965 ± 0.022 | 0.15 | PASS
LSTM | 0.704 ± 0.159 | 0.969 ± 0.014 | 0.19 | PASS
GRU | 0.747 ± 0.082 | 0.975 ± 0.006 | 0.67 | PASS
Transformer | 0.829 ± 0.069 | 0.982 ± 0.005 | 0.52 | PASS
All six deployment-feasible; highlighted row = recommended default.
· MLP is the recommended default: the Transformer's F1 edge is not real — within noise by a paired t-test (p = 0.34) and a capacity effect that reverses at matched parameters (Transformer-S 0.760, below the MLP). On the two axes that decide selection MLP is not beaten — equal F1 (0.794), better stability (best worst-fold, lowest fold variance) — at 4.5× fewer parameters.
· Latency never binds at 10 Hz — the slowest model sits >12× under the gate; model choice is a quality/stability decision, not a speed one.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
2 / 7

## Slide 3
One world core, one split, one standard — why every number here is comparable
The evaluation scaffolding shared by every model family, Weeks 2–4
Shared world dynamics
The shared world-dynamics core generates the 9-channel sensor stream (calibrated 85/15 normal/anomaly); the W5–6 RL environments import the same core, so offline data and the online env cannot drift.
Leakage-safe canonical split
Block-segmented + StratifiedGroupKFold with a 50-step purge kills window leakage at the split level. All six model families read the same fold file instead of re-deriving a split.
Two-phase fold protocol
Design choices are tuned on the canonical fold only; the locked config is retrained across all 7 fold rotations — the ledger reports mean ± std F1/AUC with per-fold columns.
Mandatory reporting standard
Split sizes · hyperparameters + seed · confusion matrix · per-class P/R/F1 · timeit latency · feasibility verdict against the platform gate for every model.
The feature lesson that carried Phase B
Cross-channel physical features (inter-wheel std, stall ratio) beat model and split tuning: +0.27 F1 on the RF baseline — before any neural model was trained.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
3 / 7

## Slide 4
Preprocessing & features — 9 raw sensors into a physics-driven 40-feature matrix
Week 2 · why the features are built for the fault mechanism, and why a plain outlier rule is not enough
Data & cleaning
15,000 steps (25 min at 10 Hz), 9 sensor channels, 15% anomaly — a causal mechanical fault (slip + stuck), not an injected burst. 0.5% sensor missingness repaired by forward/backward-fill. Torque shows zero 3σ outliers — terrain already spreads it over a wide range, so a plain outlier rule cannot separate faults from rough driving.
Feature engineering
FFT over a 50-step (5 s) window on the 4 torque channels + LiDAR captures the spectral fault signature (25 features). GPS enters as per-step deltas — absolute position is a memorised map shortcut, the delta is the transferable displacement signal. Two cross-channel physical features close the gap a per-channel view cannot: inter-wheel torque std (slip) and stall ratio (stuck). Matrix = 9 raw + 25 FFT + 6 physical = 40 features.
Dimensionality reduction (PCA)
The 40 scaled features reduce to 19 components at 95.1% variance, fit on train only. PC1 is the torque spectral centroid — the shared terrain-torque driver behind both fault types; PC2 is the stall ratio, a directly interpretable axis for the stuck mechanism.
Feature selection (RF)
Selection ranks on F1, not accuracy — with an 85% majority class, accuracy is blind to the minority. The F1 criterion keeps 5 components (val F1 0.828), slightly beating the full 19-set (0.812). Analysis only: the deployed RF keeps all 19 components.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
4 / 7

## Slide 5
Attention localises the fault (5.3× selectivity) — it does not out-detect at equal capacity
What six models on identical data, seeds and protocol actually say about the task
Capacity, not architecture, sets the ledger's top line
Param-matched Transformer-S (d_model 32): F1 0.829 → 0.760, statistically indistinguishable from the GRU (p = 0.76). MLP, GRU, RF and Transformer-S form one near-tie; only the 67.8K-parameter Transformer pokes above it, at 4.5× the MLP's weights.
Localisation is the Transformer's real differentiator
Attention mass lands on the true fault span in 98% of eligible anomalous windows — median selectivity 5.3× vs the LSTM hidden state's 1.15×. Genuine fault localisation for pointing an operator at where the fault is; an interpretability asset, not detection accuracy.
Where the residual misses live
False negatives concentrate in stuck-type faults: all four wheel torques rise together with no cross-wheel asymmetry, so steady-state stuck reads as heavy terrain. Slip-type faults are caught reliably via the engineered cross-channel features.
Stability, not ranking, is what breaks across folds
LSTM is the least fold-stable model in the ledger (±0.16 F1): one fold's val-tuned threshold collapses its F1 to 0.39 while AUC stays 0.97 on the same fold — threshold calibration, not discrimination, is the fragile part.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
5 / 7

## Slide 6
Trajectory — LSTM is best at every horizon: 1.44 cm mean, 2.18 cm at waypoint 5, 0.34 ms
Aido Humanoid · 10 steps of state → next 5 waypoints · 5,000 synthetic episodes · 5 seeds · 50 ms planning gate
Model | Mean Euclid (cm) | h5 (cm) | ms | ≤50 ms
CV extrapolation | 2.77 | 4.28 | 0.003 | PASS
Linear | 1.50 | 2.56 | 0.09 | PASS
MLP | 1.63 ± 0.06 | 2.43 | 0.03 | PASS
LSTM | 1.44 ± 0.04 | 2.18 | 0.34 | PASS
Transformer | 1.60 ± 0.15 | 2.32 | 0.51 | PASS
Mean ± std over 5 training seeds; CV / Linear are deterministic.
· The task is mostly linear — Linear wins the near waypoints (0.73 cm at h1: an optimal sway/noise filter); the whole nonlinear gain concentrates in obstacle-avoidance episodes (LSTM 2.86 vs Linear 3.52 cm at h5).
· The Transformer does not justify its latency here: slower and less accurate than the LSTM, with 3× the seed variance (±0.15); a param-matched control confirms a data-scale limit, not a tuning miss — not significant vs MLP/Linear.
· Attention over the horizon: near waypoints read the latest state, far waypoints read progressively older trend context (attention centre-of-mass step 6.7 → 3.1) — the learned analogue of a receding-horizon planner.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
6 / 7

## Slide 7
Latency never binds — quality, stability and interpretability decide deployment
Feasibility verdicts against the platform gates, and the model picks they imply
Aido Rover — 100 ms streaming gate: all six PASS
Worst model (RandomForest, 7.9 ms) sits >12× under the gate; the neural models sit 150–740× under it. Window-scaling fits put attention's breach point at hundreds of seconds of buffer — far beyond the 5 s that measured fault durations justify.
Aido Humanoid — 50 ms planning gate: all five PASS
Plan-defined gate (product docs specify 10 ms whole-body MPC / 150 ms grasp planning — discrepancy recorded, plan wins per convention); every regressor clears it by two or more orders of magnitude.
Consequence for model selection
Detection quality is a near-tie once capacity is matched, so selection falls to fold stability, cost and interpretability: MLP as the rover anomaly default · Transformer only where fault localisation is operationally worth 4.5× the parameters · LSTM for humanoid trajectory (best accuracy, lowest seed variance).
Open risk carried into Phase C
Stuck-type steady-state faults cap recall (no cross-wheel asymmetry to key on); candidate fixes — longer-horizon context or a terrain-conditioned feature — are queued behind the RL work.
InGen Dynamics · ML & NN Analyst Internship — Mid-Point Review (W1–W4)
7 / 7